## Slide 1: Android Security
GROUP MAY 1208 Alex Frisvold Alex Meyer Nazmus Sakib Eric Van Buren

## Slide 2: Advisors
Our project is through The Boeing Company and our advisor is Victor Lukasik, the manager of Boeing’s Cyber Mission Assurance group
Our faculty advisory at Iowa State is George Amariucai

## Slide 3: Problem Statement
Attempt to write a software TPM on an Android OS
To accomplish this we will use an ARM security extension called TrustZone
To safely test the TPM we must have an emulator
Notes: TPM- used to increase security by making a second chip on the processor that allows “safe world” program execution

## Slide 4: The Project
To implement a software stack that allows the emulation of the Android operating system to use the functionality of ARM’s TrustZone
This is a proof of concept project for The Boeing Corporation so they can begin development with TrustZone

## Slide 5: TrustZone
ARM’s processor extension that allows for a software TPM implementation
Available on all major ARM cell phone chips
There is limited open source development with TrustZone

## Slide 6: System Overview

## Slide 7: Application Examples of TrustZone
Secure PIN Entry
Digital Rights Management
e-Ticketing Mobile TV (Netflix)

## Slide 8: DRM Example
Notes: Many security use cases in mobile devices are related to content management
The role of a DRM agent is to enforce the access to media content based on the rights that the user has purchased.
When a user selects a DRM protected file for playback the agent must ensure that the user’s rights are still valid and, if they are, decrypt the file and pass it to the media player.
Secure world defends the DRM agent component against malicious software.
Type of attacker in this example would be the user.

## Slide 9: TPM Overview
A TPM is a chip that resides on the motherboard, and provides 4 basic functionalities
  Secure storage and reporting of platform configurations
  Protected private key storage
  Cryptographic functions
  Initialization and management functions

## Slide 10: TrustZone Implementation
There is no open source emulator for TrustZone making development difficult
We will use 4 different open source components in one modified stack

## Slide 11: QEMU
Open source hardware emulator used by Android developers
Main release does not contain TrustZone emulation capabilities
Johannes Winter is a computer scientist who modified QEMU for his own research so it can emulate TrustZone

## Slide 12: Hypervisor
Will communicate between QEMU and our two kernels, doing the context switching between them
We are still testing which one we would like to use
  NOVA, Choices, custom

## Slide 13: Fiasco Microkernel
Developed by a group at TU-Dresden
This is the only software that will run in the privileged or secure mode of the processor
Very small for security purposes

## Slide 14: L4Runtime Environment
Offers a concise set of interfaces for building applications
Comprised of low-level software components that interface directly with the microkernel
Libraries and interfaces are provided and object oriented

## Slide 15: L4Android
Derived from the L4Linux project which is developed at TU-Dresden
Designed specifically to work with Fiasco.OC microkernel
Currently runs as Android version 2.2 (Froyo) or 2.3 (Gingerbread)

## Slide 16: Android Application
The highest part of the stack will be a program we write that uses TrustZone’s TPM features
Application will make TrustZone calls to the microkernel

## Slide 17: Functional Requirement
The modified L4 runtime environment will run seamlessly over the modified Fiasco.OC microkernel
Notes: Most modifications will most likely be done to Fiasco.OC
These changes should not effect the way Fiasco.OC performs

## Slide 18: Functional Requirement
The L4Android operating system will run seamlessly over the modified L4 runtime environment

## Slide 19: Functional Requirement
Our software stack will use the secure world to provide two TPM services:
  Random Number Generation
  RSA Key Generation

## Slide 20: Functional Requirement
An Android application will be able to use the TPM services provided and will be able to perform the following tasks:
  encrypt sensitive data using the secure world
  decrypt sensitive data using the secure world

## Slide 21: Functional Requirement
Modifications made to any of the various components of the software stack should not adversely affect any of the existing functionality of the components

## Slide 22: Non-Functional Requirements
Modified software stack should runs at a usable speed
Modified software stack is stable and runs reliably
Modifications to QEMU, Fiasco.OC and L4RE should be written in C and C++ programming language on a Linux platform

## Slide 23: Testing
Make sure that Fiasco.OC microkernel will run seamlessly over Mr. Winter’s QEMU
Context switching between worlds
Writing an Android application that uses TrustZone
Notes: Lowest layer in the stack.
Correct installation on Johannes Winter’s QEMU
Make changes in the source code of the microkernel to port Fiasco to the augmented version of QEMU
Test by using Fiasco to create an ISO image and ten run it using the augmented version of QEMU
Context Switching
Switching between worlds is controlled by the Secure Monitor
Triggered by a dedicated instruction known as the Secure Monitor Call (SMC) instruction.
The world in which the processor is executing is indicated by the NS-bit in the Secure Configuration Register in the CP15, the system control processor.
In order to test if context switching between worlds is working correctly, we can check if the NS-bit is set.
Android Application
Potential to be the most difficult task because of the possibility that we may need to implement a complex TrustZone API.
The API will allow the application to communicate with the lower layers.
To test of the application works correctly, we will need to monitor calls that the application makes to the Secure Monitor and make sure that the context switching between worlds is working correctly.
The Fiasco microkernel acts as the secure monitor

## Slide 24: Difference is in Memory
Only write to memory when needed, better performance
Overwrite memory after every context switch, better security

## Slide 25: Development Environment
Host OS: Ubuntu 64-bit 10.04 LTS

## Slide 26: Considered Designs
Hypervisor solution: Hypervisor switching between two instances of the microkernel
Dual MMU solution: Two MMUs, each managing one world
Static Memory Division: Divide memory statically into two

## Slide 27: Hypervisor Solution
Two kernels monitored
by one hypervisor
One kernel in each
world
Very secure design
due to isolation of kernels
Difficult implementation

## Slide 28: Dual MMU Solution

## Slide 29: Static Memory Division

## Slide 30: Difficulties Encountered
Lack of good documentation
Proprietary nature of many relevant details
Inexperience with technologies
Time constraints

## Slide 31: Accomplishments
Discovered and documented problems
Several designs for an implementation
Built ARM images of Fiasco, L4Re and L4Linux
Good starting point for another team

## Slide 32: Future Directions
Senior Design project
Boeing software development
Open source community